Posted: Wed, May  2, 1990   4:06 AM PST              Msg: BGJA-4244-6234
From:   UOSAT
To:     DOCS
Subj:   UO-14 PCE TELEMETRY FORMAT

UoSAT-OSCAR-14 PACSAT Communications Experiment Telemetry Format

Telemetry is used to monitor the state of experiments and housekeeping
subsystems onboard the satellite.  In particular, it measures voltages,
currents, temperatures and the status of digital switches.

The PCE transmits telemetry in AX.25 UI frames at 9600 bps.  A "packet" of
telemetry is wholly contained in the information field of a single UI frame.
Each packet contains a timestamp indicating when the samples were taken, the
the data samples (including additional information detailed below), and a CRC.
The CRC is provided because the link between the KISS TNC used to receive the
UI frames and the computer used to display or analyze the telemetry may become
unreliable at high data rates.  Thus the telemetry packet format is:

<timestamp> <data> [<data>...] <crc>

All of this is contained WITHIN the AX.25 UI frame information field.  The
information field will not exceed 256 bytes in length.

In addition to the fields contained in the telemetry packet, the receiving
process must maintain a <channel> variable.  The use of this variable becomes
clear below.

Interpretation of the fields is as follows:

BYTE ORDER

All multi-byte values are stored least significant byte first.  Where bits
are numbered, bit 0 is the least significant bit of a byte or multi-byte
value.

TIMESTAMP

The <timestamp> is a 4-byte, unsigned integer representing the number of
seconds since 0000 UTC January 1, 1970.  This is the UNIX standard time,
and is also the format for times under the draft ANSI C standard.

DATA

Each <data> item is a 2-byte, unsigned integer, with internal encoding as
follows:

bits 0  - 11     A 12-bit <value> field
bits 12 - 15     A 4-bit <type> field

The <type> field tells the receiver how to interpret the <value> field, and
what other action to take.  The following <type> items are defined:

       bit
    15 14 13 12         Interpretation and Action
    -- -- -- --         --------------------------
     0  0  1  0         <value> is a channel number.
                        Initialize <channel> variable to <value>.

     0  0  0  1         <value> is the telemetry sample for current <channel>.
                        Do not increment <channel> after processing <value>.

     0  0  0  0         <value> is the telemetry sample for current <channel>.
                        Increment <channel> after processing <value>.

All other types are currently undefined and should be ignored.

The first <data> item in a telemetry packet will always be of type 0010, to
initialize the channel variable.

CRC

The cyclic redundancy check is provided as protection against errors on the
link between the receiving TNC and the computer which is processing the
telemetry.  It is the XMODEM CRC algorithm encoding all bytes, from the
first byte of the <timestamp> to the last <data> byte.

ADDRESS and PID

We are currently transmitting these frames with an AX.25 Protocol
Identification byte of 0xf0.  The source address is UOSAT3-0 and the
destination address is TLM-0.


EXPLAINATION and EXAMPLES

In the examples, assume that the <timestamp> is 2638d6ce hexidecimal. (From
here on, hexidecimal numbers are indicated by a leading 0x.)

You will see that this packet format allows us to efficiently encode the
most common type of telemetry "frame" - e.g. a frame in which we begin with
channel 0 and increment through the channel numbers.  In this case, the
packet starts out with:

0x2638d6ce    /* timestamp */
0x2000        /* <type>=0010, <value>=0 */
              /* so set your channel variable to 0 */

and then proceeds with the data for each channel, with the <type> bits
indicating "increment" (0000). For example, if channel 0 is at a value of
0x496 and channel 1 is at 0x003, we have

0x2638d6ce    /* timestamp                      */
0x2000        /* set your channel variable to 0 */
0x0496        /* value of channel 0 and increment channel to 1 */
0x0003        /* value of channel 1 and increment channel to 2 */

Etc.

However, on UO-14 (as on UO-11) we have some "submultiplexed channels".
The primary example is channel number 15 which; every 12 times it is read
it returns voltages for the 10 cells of the battery and two 0 values for
synchronization.  Ideally we would have the PCE read the channel 12 times
for each telemetry packet and transmit all 12 values.  This is why the
"display but don't increment" <type> (0001) is defined.  So, now, in our
frame we have

0x2000        /* set your channel variable to 0                  */
0x0496        /* value of channel (0) and increment channel to 1 */
0x0001        /* value of channel (1) and increment channel to 2 */
 ...          /* 13 other <data> items with "increment" type.    */
 ...          /* leaving the channel variable at 15              */
0x10nn        /* first submultiplexed battery cell sample        */
0x10nn        /* second submultiplexed battery cell sample       */
 ...          /* and so on, until the last of the 12 samples,    */
0x00nn        /* which is of "increment type.                    */

We can also "jump over" any unwanted channels in the frame by inserting
another "set your channel variable" data entry.  This is done on UO-14 to
skip the blank channels between analog telemetry and digital status points.

So we have a flexible and efficient encoding system which does not require
the transmission of every channel number, yet permits submultiplexing and
channel number jumping.  In the case of UO-14, where the native telemetry
samples are 12-bits, we have "wasted" only 4 bits per channel on
supervisory information to arrive at this flexibility.


SAMPLE FRAME

A hex dump of the data in a telemetry packet from the UO-14 engineering
model is reproduced below.  It includes use of all features: 3 "set channel
variable" entries (one at the beginning of the frame and 2 to jump over
unwanted channels), 12 consecutive samples of channel 15 and 56 other
samples.  The CRC is also correct.

      CE D6 38 26 00 20 00 00 16 02 37 00 07 00
CF 01 CF 01 CF 01 08 02 00 00 49 02 CB 00 2A 00
CF 01 CF 01 F4 01 33 12 32 12 30 12 2B 12 29 12
27 12 22 12 24 12 00 10 00 10 3A 12 34 02 00 00
6D 00 81 02 34 00 CF 01 CF 01 C8 01 81 01 54 01
2C 00 C7 01 04 03 CF 01 CF 01 CF 01 E6 01 B0 00
03 01 36 01 5D 01 6A 01 A1 01 CB 01 28 20 00 00
00 00 00 00 00 00 8F 01 FB 01 10 02 55 02 DD 00
40 20 80 00 00 08 02 00 80 00 12 08 83 00 10 04
08 08 00 08 AB A8


XMODEM CRC

The XMODEM CRC receive checking is defined using the following C code:


unsigned short crc;              /* global crc register.              */
crc = 0;                         /* clear crc register                */
for (all received data bytes)
    gen_crc(rx_byte);            /* crc the incoming data bytes       */
gen_crc(1st_crc_byte);           /* crc the incoming first crc byte   */
if(gen_crc(2nd_crc_byte))        /* crc the incoming second crc byte  */
        bad_crc();               /* non-zero crc reg. is an error     */
else
        good_crc();              /* zero crc is a good packet.        */

/* Function to take a byte and run it into the XMODEM crc generator.  */
/* Uses a global CRC register called "crc".                           */
gen_crc(data)
char data;
{
    int y;
    crc ^= data << 8;
    for(y=0; y < 8; y++)
        if( crc & 0x8000)
            crc = crc << 1 ^ 0x1021;
        else
            crc <<= 1;
    return crc;
}


Further information on generation of XMODEM CRC via more effecient byte-wise
methods can be found in BYTE Magazine,  September 1986, pp. 115-124.


CONCLUSION

Your comments are solicited - especially relating to any errors in this
document.  Address them to

Packet: G0K8KA @ GB3UP
Telemail: UOSAT
Other nets: ELE001@UK.AC.SURREY.SYSD

or, last resort

Jeff Ward, G0/K8KA
UoSAT Unit
University of Surrey
Guildford, Surrey GU2 5XH
United Kingdom

-----------------------------

Comments may also be forwarded via CIS by NK6K 71635,1174